## Slide 1
Goal: Optimize battery operation for revenue while minimizing degradation
Scope: Frequency Regulation market participation
Slave controller (RL)
Generalized Policy Search (GPS)
Environment: Complex DAE-based battery model Simplified ODE-based model
Modularized Environment
NN – Based
Reward function (Same as before):
27 June 2025

## Slide 2
Implemented without cf penalty
As expected:
  High FR band
  High Grid usage
  Fast degradation
Results
EOL limit: cf=1.4

## Slide 3
Master controller (MPC)
Goal: Minimize battery degradation
Receives new states every time horizon
Set new constraint for every time horizon
MPC
RL
Env
Cons
Act
Reward
State
min cf
max revenue
Main issues:
  Infeasibility Fallback constraints strategy
    Problem: chain of non-convergence
    Solution?: Dynamic conservative fallback based
          on degradation rate
  High Computational Cost
    15 policy population, 7 epochs, time horizon 3h = 9 hour!
  For every generation
  For every Policy
  Solve MPC with nonlinear cons
  end
  end
Break if cf > cf_max
State

## Slide 4
Solution?:
  Upsampling (Already implemented):
    Increased MPC timestep to 6 seconds
    Fewer time interval
  Already using low fidelity and linear objective
  Warm start for RL and MPC (Already implemented)
  Implement PSO algorithm from Bloor’s work
Test:
  8 policies, 5 generation
  Increased degradation rate from 1e-9 (original) to 1e-6